## Slide 1: Spatialization

## Slide 2: A head-related transfer function (HRTF)
is a response that characterizes how an ear receives a sound from a point in space; a pair of HRTFs for two ears can be used to synthesize a binaural sound that seems to come from a particular point in space. It is a transfer function, describing how a sound from a specific point will arrive at the ear (generally at the outer end of the auditory canal).
Humans have just two ears, but can locate sounds in three dimensions – in range (distance), in direction above and below, in front and to the rear, as well as to either side. This is possible because the brain, inner ear and the external ears (pinna) work together to make inferences about location.

## Slide 3: HRTF cues
Humans estimate the location of a source by taking cues derived from one ear (monaural cues), and by comparing cues received at both ears (difference or binaural cues). Among these interaural (between the two ears) difference cues are the differences of arrival time (ITD) and differences of intensity (IID). The monaural cues come from the interaction between the sound source and the human anatomy, in which the original source sound is modified before it enters the ear canal for processing by the auditory system. All these modifications encode the source location, and may be captured via an impulse response termed the head-related impulse response (HRIR). Convolution of an arbitrary source sound with the HRIR (binaural encoding) converts the sound to what would have been heard by a particular listener if it had been played from a particular source location. The HRTF is the Fourier transform of HRIR. A binaural microphone (with or without Kunstkopf Fritz) is the other method of creating binaural recordings.
Vav (The Hub) – binaural encoded
Talking Drum - CNMAT Tennis Court –
Binaural recording

## Slide 4: Ambisonics - Surround Sound
The Soundfield microphone is an audio microphone composed of four closely spaced subcardioid or cardioid (unidirectional) microphone capsules arranged in a tetrahedron. It was invented by Michael Gerzon and Peter Craven, and is a part of, but not exclusive to, Ambisonics, a surround sound technology.
A Soundfield microphone kit, consisting of the microphone and a signal processor, produces two distinct sets of audio signals called A-Format and B-Format.

## Slide 5: A and B formats
The A-Format is the signals from four microphones on the faces of a tetrahedron. The first set, the A-Format, is produced by the Soundfield microphone itself and consists of the four signals from the microphone capsules. These four signals are not intended to be used without further processing. The A-Format is normally transformed into the second set of audio signals, the B-Format. The B-Format is the standard audio format produced by a soundfield kit. It consists of the following four signals:
• W - a pressure signal corresponding to the output from an omnidirectional microphone
• X - the front-to-back directional information, a forward-pointing velocity or "figure-of-eight" microphone
• Y - the side-to-side directional information, a leftward-pointing "figure-of-eight" microphone
• Z - the up-to-down directional information, an upward-pointing "figure-of-eight" microphone
These are the constant (W) and linear (X, Y, Z) terms in the multipole expansion of a function on the sphere – in effect, it approximates the wave field on a sphere around the microphone. The B-format recording can be decoded to any number of speakers arranged in both the horizontal and vertical planes.

## Slide 6: Ambisonics terminology
In Ambisonics the term "periphony" (literally, "sound (around) the edge") is frequently used to denote full-sphere, with-height, 3-dimensional surround – note that in a periphonic system virtual sources can be localised anywhere within the sphere, not only at its surface.
Strictly speaking, we should define a difference between "with-height" and "periphony". The former implies the ability to (re)create a sensation of sounds coming from above the listener, and/or a sensation of space above the listener. "Periphony", however, strictly denotes full-sphere production, which includes height and depth, providing the ability to place sounds in any direction including below the plane of the listener.
The term "planar" (on a single plane, i.e. no height, or 2-dimensional) is used to refer to horizontal-only Ambisonics; the term "pantophonic" will also be found with the same meaning. Also, in this field; "2-D" and "3-D" respectively mean planar & periphonic.

## Slide 7: Comparison with conventional surround
A significant difference between Ambisonics and other surround systems is that the signal is the same irrespective of the number of speakers connected to the decoder, or where they are. The decoder and speaker array do their best to render the original soundfield to the highest resolution of which the system is capable.
Conventional surround, however, maps one speaker to one channel. Thus each speaker (or channel) has a name based on its physical location (such as "left rear" or "right front"). In Ambisonics, it doesn't matter where the speakers are, it's the direction that's important, and the fact that the speakers are all required and working together to localize virtual sources. So we may talk about a source coming from so many degrees from center front, or from compass directions, where center-front is North. Thus while a typical surround "walk-around" or channel identification test will simply drive each speaker in turn and label the speaker from which listeners should be hearing sound, the Ambisonic equivalent will often call out angle directions, so listeners can check that the virtual source really is coming from that direction.